## Slide 1
Thank You for Attending Today’s Webinar:
Your Host
Matt DeLacluyse Operations Manager RAECO Rents mattd@raecorents.com
Featured Speaker
Tim Johnson Business Development SciAps tjohnson@sciaps.com
How to use an XRF Handheld for sampling lead paint and more

## Slide 2: What you already know
Toxic elements are everywhere
  Food
  Water
  Toys
  Soil
  Paint

## Slide 3: Analysis techniques for these elements
Laboratory
  AA
  ICP
  ICP-MS
Typical turn around time – 1-2 weeks

## Slide 4: In the field
Handheld XRF
  Many models on the market
  Near instantaneous results
  Don’t have to disturb the material

## Slide 5: Handheld XRF for lead paint
Only 2 HUD-accepted models currently on the market
Typically use radioactive source
  Cd-109
  Co-57
Cost of owning prohibitive
Somewhat difficult to rent due to regulatory and stock concerns

## Slide 6: Why is it tough to rent?
Radioactive sources must be replaced
  Half-life of Cd-109 is 461 days
  Half-life of Co-57 is 272 days
Many shipping companies will not accept due to radioactive materials

## Slide 7: The solution
SciAps X-550
The only HUD-accepted lead paint analyzer that does not contain radioactive material

## Slide 8: Why the X-550 Pb?
No radioactive materials
HUD accepted PCS sheets at 0.5, 0.7, and 1.0 mg/cm2 with no inconclusive ranges
Fewer regulatory burdens
Can do soil, alloy identification and lead paint using the same instrument

## Slide 9: So how does it work?
X-Ray tube
Uses either Au or Rh anode to produce the X-rays.
No proximity button to fail

## Slide 10: I think I have heard this before
Innovex released a tube-based analyzer with a PCS around 2006
PCS had large inconclusive range
Sold to Olympus who no longer produces it

## Slide 11: New Technology Brings Improved Performance
SDD gives smoother baseline
Use of L-gamma improves x-ray escape 300X

## Slide 12: What the heck is a PCS?
Performance Characteristic Sheet
Shows how well the instrument is able to determine lead concentrations in paint on different substrates and at different depths
Run by a 3rd party
Filed and published with United States Department of Housing and Urban Development

## Slide 13: Why would I care about a good PCS?
The PCS shows if there is an inconclusive range.
If the reading falls in the inconclusive range, a paint chip must be sent to the lab.
AND THEN YOU WAIT

## Slide 14: Are radioactive materials a big deal?
All instruments on the market are well-shielded and should be safe
QUESTIONS THOUGH:
How old is the source in the instrument you are trying to use?
Are you ok with a 30 second analysis time?

## Slide 15: How can this help me?
One analyzer for most of your elemental analysis
Only carrying one case instead of one to look for lead paint, and another to analyze the soil.
Same analysis speed no matter the age.
No proximity switch, so irregular shaped objects can be analyzed.

## Slide 16
What does OSHA say about this?

## Slide 17: OSHA
OSHA does not recognize any amount of lead as being safe
OSHA does not recognize any handheld technique as being confirmatory for lead-free
Handheld XRF can be used to help determine the level of PPE required

## Slide 18: Is it really that easy?
100 year old church in Massachusetts
One click on the trigger
Analysis time of 6 seconds

## Slide 19: Example
Thick paint sample from old MA home,
Nearly ¼” of paint thickness.
High Zn, Ba and TiO2 paints on top of lead.
Previous L-shell methods fail because there’s no lead L-alpha signal, so no way to correct lead results. Yield false negative.
The SciAps unit with X-ray tube and SDD detector measures the lead L-gamma line.
Correction made from L-beta and L-gamma.
Key: L-gamma is about 300 times more penetrating than L-alpha in a highly absorbing paint matrix like ZnO and BaO.

## Slide 20: In the field
Start-up about 1 minute
Calibration 15 seconds
Cal check 30 seconds
Off and running

## Slide 21: Screen Results

## Slide 22: Sample csv Report
Date | Test # | Pass/Fail | Unit type | Calibration Model/ Matrix ID | Display Sigma | LOD Sigma | Pb | Pb +/- | Pb P/F | Job Number | Room | Room Choices | Structure | Choice | Substrate | Wall | Location | Condition | Condition Choices
######## | 46 | Pass | mg/cm2 | PCS Cal | 1 | 3 | 1.06 | 0.04 | Positive |  |  |  |  |  |  |  |  |  | 
######## | 47 |  | mg/cm2 | LeadPaint | 1 | 3 | 1.01 | 0.01 | Positive |  |  |  |  |  |  |  |  |  | 
######## | 48 |  | mg/cm2 | LeadPaint | 1 | 3 | 1 | 0.01 | Positive |  |  |  |  |  |  |  |  |  | 
######## | 49 | Pass | mg/cm2 | PCS Cal | 1 | 3 | 1.02 | 0.03 | Positive |  |  |  |  |  |  |  |  |  | 
######## | 50 |  | mg/cm2 | LeadPaint | 1 | 3 | 1.18 | 0.05 | Positive |  |  |  |  |  |  |  |  |  | 
######## | 51 | Pass | mg/cm2 | PCS Cal | 1 | 3 | 1.08 | 0.04 | Positive |  |  |  |  |  |  |  |  |  | 
######## | 52 |  | mg/cm2 | LeadPaint | 1 | 3 | 1.02 | 0.01 | Positive |  |  |  |  |  |  |  |  |  | 
######## | 53 |  | mg/cm2 | LeadPaint | 1 | 3 | 1.12 | 0.05 | Positive |  |  |  |  |  |  |  |  |  | 
######## | 54 |  | mg/cm2 | LeadPaint | 1 | 3 | 0 | 0.01 | Negative | 333 |  |  | Bookcase | Shelf |  |  |  |  | 
######## | 55 |  | mg/cm2 | LeadPaint | 1 | 3 | 0 | 0.01 | Negative | 333 |  |  |  |  |  |  |  |  | 
######## | 56 |  | mg/cm2 | LeadPaint | 1 | 3 | 0 | 0.01 | Negative | 333 |  |  |  |  |  |  |  |  | 
######## | 57 |  | mg/cm2 | LeadPaint | 1 | 3 | 0 | 0.01 | Negative | 333 | Single Fam House | Vestibule | Trim |  |  |  |  | Intact | 
######## | 58 |  | mg/cm2 | LeadPaint | 1 | 3 | 0 | 0.01 | Negative | 333 | Single Fam House | Vestibule |  |  |  |  |  |  | 
######## | 59 |  | mg/cm2 | LeadPaint | 1 | 3 | 0 | 0.01 | Negative | 333 | Single Fam House | Vestibule |  |  |  |  |  |  | 
######## | 60 |  | mg/cm2 | LeadPaint | 1 | 3 | 0.05 | 0.01 | Negative | 333 | Single Fam House | Vestibule |  |  |  |  |  |  | 
######## | 61 |  | mg/cm2 | LeadPaint | 1 | 3 | 0.04 | 0.01 | Negative | 333 | Single Fam House | Vestibule |  |  |  |  |  |  | 
######## | 62 |  | mg/cm2 | LeadPaint | 1 | 3 | 0 | 0.01 | Negative | 333 | Single Fam House | Vestibule |  |  |  |  |  |  | 
######## | 63 |  | mg/cm2 | LeadPaint | 1 | 3 | 2.96 | 0.13 | Positive | 333 | Single Fam House | Vestibule |  |  |  |  |  |  | 
######## | 64 |  | mg/cm2 | LeadPaint | 1 | 3 | 2.88 | 0.13 | Positive | 333 | Single Fam House | Vestibule |  |  |  |  |  |  | 

## Slide 23
Quick Demonstration

## Slide 24: Technology to help you
Bluetooth, Wi/Fi, USB interfaces
Micro Camera for assuring proper location
Macro Camera for adding location images
Results exported in .csv or .pdf with no special software needed

## Slide 25: What about other elements in paint?
Currently not able to analyze other elements in buried paint
Soil mode will allow surface elements to be analyzed

## Slide 26: Steps for a total assessment
Analyze painted surfaces for lead
Analyze soil for lead and other toxic elements
Analyze water for lead

## Slide 27: Water….really?
Dr. Marya Lieberman at Notre Dame
  Good results with concentrating lead from water onto filters
  Developed kits for use with XRF
  https://pubs.acs.org/doi/abs/10.1021/acs.analchem.9b05058

## Slide 28: What’s next?
  Dust wipes
    Enable client to check that cleanup is complete
  Air Filters
    Check for indoor air quality
  ???

## Slide 29
Questions?

## Slide 30
Get Social with RAECO Rents
www.linkedin.com/company/raeco-rents
@RaecoRents
www.youtube.com/user/RaecoRentsVideos